## Slide 1: The Craft of Tree Felling
Alan Hale
June 2024

## Slide 2: Outline
Felling in the Direction of Slight Lean
Facing Issues Felling Difficult Trees

## Slide 3: Sizeup
Search for overhead hazards
Debris
falling from above causes over one-half of all felling accidents
Practice watching overhead while cutting
Occasionally glance at the saw, kerf, and top of the tree
Check for snags (standing dead or dying tree)
  Snags may fall at any time due to wind or vibration from a felled tree
  Cut any snags in the felling area first
Swamp out the base
  Remove all material that could cause sawyers to lose their balance
Many fatalities have occurred because the
sawyer could not move
far enough away from the stump
to avoid being struck or pinned
Assess the tree’s lean
  The tree has two natural leans: head lean and side lean
  Project a vertical line from the center of the tree’s stump
  Use two different locations at right angles to each other
Check for soundness of the holding wood
  Bore a hole with a cordless electric drill or the chain saw
  Evaluate the wood quality from:
    Color of the sawdust and
    Ease of penetration

## Slide 4: Felling In The Direction Of Slight Lean ( Conventional Face Cut )
Stump Shot 2-5 Inches
D
Holding Wood
10% of D
1
2
3
1/3 D
Kerf
Execute the cuts standing or on one knee with the saw at waist level
Felling Direction
Lean Direction
Face Cuts
1 2
Back Cuts 3
Holding Wood or Hinge Wood (HW)
Vertically oriented wood connecting the stump to the tree
HW

## Slide 5: Felling Mechanics
Height of holding wood -- stump shot or anti-kickback device
–
–
Prevents kickback from tree rotating about its center of mass Prevents kickback when striking another tree in standing timber
•
Width of holding wood – tree hinged to the stump while falling
–
–
Controls the direction and fall of the tree
Without holding wood the tree is unguided during the fall
•
Holding wood severed when the two face cuts meet
Face should not close until the tree
  Fully committed to the fall
  Falling in the desired direction
–
Improper facing (face cut too shallow, etc.)
•
•
Holding wood breaks early (unguided fall) Loss of tree placement control
D
Height Stump Shot
Anti-Kickback Device
Horizontal or Gunning Cut
Width Hinging
45o
Sloping Cut
Back Cut
Holding Wood
Facing

## Slide 6: Significance of Stump Shot View One of Five
Stump Shot
Back & Gunning Cut in Same Plane
HW
HW
Back Cut & Gunning Cut On Different Plane
Back Cut & Gunning Cut On Same Plane

## Slide 7: Significance of Stump Shot View Two of Five
Stump Shot
Back & Gunning Cut in Same Plane
HW
HW

## Slide 8: Significance of Stump Shot View Three of Five
Stump Shot
Back & Gunning Cut in Same Plane
HW
HW
Felling Tree Strikes Another Tree
Felling Tree Strikes Another Tree

## Slide 9: Significance of Stump Shot View Four of Five
Stump Shot
Pow
Back & Gunning Cut in Same Plane
HW
HW Breaks Prematurely

## Slide 10: Significance of Stump Shot View Five of Five
Stump Shot
Stump Shot Prevents Kickback Of The Felled Tree
Felled Tree May Hit Sawyer Due To Kickback
Back & Gunning Cut in Same Plane
Pow
HW
HW
HW Breaks Prematurely
HW Breaks Appropriately When Sloping & Gunning Face Meet

## Slide 11: Three Kinds of Faces
Open Face
Conventional Face
Humboldt Face
70o to 90o
45o
45o
1/3 of D
1/3 of D
1/3 of D
Tree Hits Ground
Middle of Fall
Middle of Fall
2-5 inches Above Face Intersection
2-5 inches Above Gunning Cut
2-5 inches Above Gunning Cut
Total Angle
Depth
Face Closure Back Cut
Comments
Greatest Control Provided by Hinge Wood
Greatest Accuracy in Constructing the Face Cuts
Greatest Saving of Lumber
D
D
D
HW
HW
HW

## Slide 12: Facing The Tree
( Conventional Face Cut )
Always mark the location of holding wood before making face cuts!
•
•
Sloping cut
Sloping cut is at a 45o angle to the horizontal (goal)
End with the saw blade horizontal
•
Gunning cut
Set your dogs on the bottom-face corner of the rectangle
Make the gunning cut (dictates the direction of tree fall)
–
Difficult to make the gunning and sloping cut meet
•
•
Sight down the kerf of the sloping cut Set a straight stick out of the kerf to sight
•
Check
The sloping and gunning cuts must not overlap (Dutchman) Re-cut the sloping cut to correct misalignment
The face cuts must be cleaned out to prevent premature face closure
–
–
–
– Verify that the re-cuts do not alter the felling direction
–
If the re-cuts will cause the face to extend too far into the tree, end the sloping cut directly
over the gunning cut (fixed)
D
D
D
Goal
Dutchman
Fixed

## Slide 13: Back Cut With A Slight Lean in the Felling Direction
•
•
•
•
•
•
Back cuts 2-5 inches above and parallel to the gunning face cuts Remove bark around wedges to improve lifting effectiveness
A single wedge with wind can sever holding wood (rocking action) Do not drive the wedges hard (create heavy leaner)
Every 3-6 inches of back cut re-tighten the wedges (use an ax) Wedges are used (in general) to prevent the tree from sit-back due to
–
–
–
Incorrect estimate of lean Strong winds
Felling the tree in a different direction from the tree’s natural lean
Holding Wood
Back Cut
Face Cut
Holding Wood
Back Cut
Face Cut
Wind Reduces Stability Stable Configuration
Lean and Felling Direction

## Slide 14: Escape Routes
Danger Zone
Danger Zone
Danger Zone
Back Cut
Face Cuts
Holding Wood
Escape Route
Escape Route
Escape Route
Prepare two escape routes
Minimum of 20 feet from stump
45o to the sides and back
Use large tree or rock for protection
Felling Direction
Never Attempt to Escape Directly Behind the Tree

## Slide 15: Markup Before Cutting
Mark & paint horizontal ref plane
Identify felling direction
Mark 1/3 diameter edges
Mark top of sloping cut
Paint sloping cut (optional)
Mark & paint horizontal back cut plane
Mark sloping cut
Make gunning cut
Mark holding wood (back edge)
Make back cuts
Mark Horizontal Plane
Mark 1/3 D, Sloping, & Back Cut Plane
Insert Sighting Stick Into Kerf
Felling Direction
1/3 D
Top of Sloping Cut
Ref Plane
Back Cut Plane
Gunning Cut
Small Diameter Chord
Sighting Stick
Holding Wood
(Back Edge)

## Slide 16: Felling The Tree (Summarize)
•
•
Mark cut locations with surveyors' paint (visually plan felling approach) Face the tree (two planar cuts)
Select a face cut type: open, conventional, Humboldt
Always located on the desired felling direction side of the tree
Check face location with a horizontal line centered and perpendicular to the intersecting face cuts
Re-cut if necessary
Execute the back cut (minimum of one cut)
Most are on the same plane
2-5 inches above the face intersection cuts (establish stump shot)
Maintain holding wood (hinge wood)
Use wedges, jacks, and special back cuts to correct for lean
Watch overhead as a priority with quick glances elsewhere Escape the stump when the tree commits to the fall
Quickly follow a predetermined escape route
Do not hesitate at the stump attempting to cutting more wood
If the saw becomes stuck leave it
If the saw prevents a rapid escape drop it
•
•

## Slide 17: Outline
Felling in the Direction of Slight Lean
Facing Issues Felling Difficult Trees

## Slide 18: Improper Facing Issues
•
Barber-chair split
–
–
–
No face cuts (only back cut) Kerf face (saw blade thickness) Face cut < 1/3 the tree diameter
•
Felling control lost
–
–
Dutchman cut across the entire face Sloping and gunning angle too shallow
•
Felling direction altered
–
–
–
Vertically angled face cut Dutchman cut only on one side Face not cleared out on one side

## Slide 19: No Face Cuts (Only Back Cut) ( Improper Facing – Barber-chair Split )
•
•
•
•
•
No Face Cuts Barber-Chair Split
The back cut progresses without facing
Eventually the tree falls faster than the back cut progress Tree will always barber-chair split
Tree kick back extremely dangerous to the sawyer
Quality of the wood greatly reduced due to the vertical split
D
Tree
Kick back
D
Back Cut
Any Tree Can Be Felled Without Facing – Costly And Dangerous

## Slide 20: Kerf Face (Saw Blade Thick) ( Improper Facing – Barber-chair Split )
•
•
•
•
•
D
Back Cut
Face Cut
Shallow Face Cut Barber-Chair Split
Face closes quickly
Tree falls much faster than the back cut progress Tree will always barber-chair split
Tree kick back extremely dangerous to the sawyer
Quality of the wood greatly reduced due to the vertical split
Tree Kick back
D

## Slide 21: Face Cut < 1/3 The Tree Diameter ( Improper Facing – Barber-chair Split )
•
•
•
•
Small face opening is ineffective at directing the tree Holding wood is either broken or torn out
Loss of control early in the felling process Tree likely to barber-chair
Facing Cut Too Shallow
D
Back Cut
Face Cut
Desired Felling Direction
HW
Back Cuts
Actual Felling Direction
Actual Felling Direction
Face Cuts

## Slide 22: Dutchman Cut Across The Entire Face ( Improper Facing – Felling Control Lost )
•
Dutchman definition
One of the face cuts extends beyond the other face cut
Face within a face
Dutchman tree felling mechanics
Dutchman closes
  Tree splits vertically (barber-chair)
  Holding wood breaks off unevenly
Felling control lost
Weak tree might snap anywhere along its length
•
D
D
Sloping Face Dutchman
D
Result of the Dutchman
Barber-Chair Split
Gunning Face Dutchman

## Slide 23: Sloping & Gunning Angle Too Shallow ( Improper Facing – Felling Control Lost )
•
•
•
•
Face closes prematurely
HW is broken or barber-chair (very similar to a Dutchman cut) Tree could jump off of the stump when HW is broken
Loss of control early in the felling process
Facing Angle Too Small
D
Back Cut
Face Cut
Face Cuts
Desired Felling Direction
HW
Back Cut
Actual Felling Direction
Actual Felling Direction

## Slide 24: Vertically Angled Face Cut ( Improper Facing – Felling Direction Altered )
•
The highest part of the face closes first
–
–
Pivots the tree toward the open part of the face The highest HW breaks behind the closed faces
•
The HW behind the lower part of the face
–
–
Continues to hold
Pulls the tree to the longer HW
•
Loss of felling control
Gunning Cut
Sloped Face Cuts
Desired Felling Direction
Actual Felling Direction
Face Cuts
HW
Back Cuts
Highest HW Breaks
Highest HW Breaks
D
Back Cut
Face Cuts
Sloping Cut

## Slide 25: Dutchman Cut Only On One Side
Felling process unconstrained by the side of the tree with no HW
The HW side of the tree secures the tree to the stump
–
–
Pulls (pivots) the tree to the HW side of the tree HW is eventually broken when the face cuts close
•
•
Tree does not fall in the desired direction (loss of felling control)
Used for felling trees in a direction different from natural lean
– Concept behind swing Dutchman
Desired Felling Direction
Face Cuts
HW
( Improper Facing – Felling Direction Altered )
Actual Felling Direction
HW Cut On One Side
Back Cuts
Sloppy Face Cut (HW Lost)

## Slide 26: Face Not Cleared Out On One Side ( Improper Facing – Felling Direction Altered )
•
•
•
•
•
One side of the face closes on the obstruction The hw behind the obstruction is broken
The HW on the other side of the tree pulls the tree in that direction But tree does not fall in the desired direction (loss of felling control)
Used for felling trees in a direction different form natural lean
– Concept behind step Dutchman
Obstructed Face
Desired Felling Direction
Actual
Felling Direction
Face Cuts
HW
Back Cuts
D
Back Cut
Face Cuts
HW
Chainsaw Bar Too Short (Obstruction)

## Slide 27: Outline
Felling in the Direction of Slight Lean
Facing Issues Felling Difficult Trees

## Slide 28: Significance of Tree Diameter
Moderate To Large Diameter Trees Small Diameter Trees
Chainsaw bar too short to reach completely across the stump
Not enough room for chainsaw bar and wedges in the kerf
Difficult to execute back cut fast enough to prevent loss of control or barber-chair
Difficult to prevent sit-back
Face Cuts
HW
Back Cuts
Saw
Blade
Actual Felling Direction
Desired Felling
Chainsaw Blade Too Short
Direction
Natural Lean
Face Cuts
HW
Back Cuts
Saw
Blade
Desired Felling Direction
Natural Lean
No Room For Wedges
?
Unwanted HW

## Slide 29: Felling Difficult Trees ( Moderate to Large Diameter )
•
Head Lean Heavy
•
Opposite of Head Lean Slight
•
Opposite of Head Lean Heavy

## Slide 30: Head Lean Heavy (Side-boring)
•
The trigger cut (8) (made in the felling direction)
–
–
Releases the tree to fall without pinching the saw blade Allows sawyer and saw blade to readily escape the falling tree
Holding Wood
Back Cuts
Felling Direction
Lean Direction
Maintain Holding Wood
6
5
7
8
5
6
7
8
D
Cleavage Line
1
2
Face Cuts
1 2
3
4
Face the tree in the felling direction (1 & 2)
Clip outside holding wood on each side to prevent side scarring (3 & 4)
Bar is pushed straight in on both sides (5 & 6) (leave holding wood)
Continue the back cut in the opposite direction of the face (7)
  Stop the back cut short of the tree falling
  Remove the saw blade before the back wood is severed
3 4
Cleavage Line

## Slide 31: Opposite of Head Lean Slight
•
•
•
•
•
•
•
Face the tree in the felling direction (1 & 2) Start the back cut (3)
Insert two wedges when room is available
Remove bark around the wedges to improve lifting efficiency Drive wedges alternatively until they are tight
Re-tighten the wedges every 3-6 inches of back cut
Continue the process until tree tips forward (do not cut holding wood)
Holding Wood
Back Cut
Felling Direction
Lean Direction
D
Face Cuts
1 2
Maintain Holding Wood
1
2
3
3
Saw Blade
Saw Blade

## Slide 32: Opposite of Head Lean Heavy
Face the tree in the felling direction (1 & 2)
Start the back cut (3)
Cut the hydraulic jack footing (4) (measure down from the back cut)
Remove bark around the wedge locations to improve lifting efficiency
Insert hydraulic jack with bearing plate & two wedges for lifting stability
Raise the jack and re-tighten the wedges (every 3-6 inches of back cut)
Multiple jacks may be necessary (always use wedges for stability)
Continue the process until tree tips forward (do not cut holding wood)
Holding Wood
Back Cut
Felling Direction
Lean Direction
D
Maintain Holding Wood
Hydraulic Jack and Footing
Wedge 2
Wedge 1
Wedges
Bearing Plate
1
2
Face Cuts
1 2
3
3
4
4

## Slide 33: Felling Small Diameter Trees
•
Head Lean
Divided back cut Opposite Head Lean
Back cut first Head or Back Lean
Slot through holding wood
•
•

## Slide 34: Head Lean -- Small Diameter Tree ( Divided Back Cut )
Maintain Holding Wood
Holding Wood
1
2
3
Natural Falling Direction
•
•
Face the tree in the felling direction (1 & 2) Cut half of the total back cut (3)
–
–
Watch out for saw kickback Maintain holding wood (HW)
•
Place a small wedge in the kerf
–
–
Located at least one inch from the remaining back cut Wedge will prevent the tree from setting back (wind)
•
Finish with back cut (4) (watch out for saw kickback and maintain HW)
–
–
Head lean slight – normal back cut (back of tree to HW) Head lean heavy – side-boring back cut (HW to back of tree)
Felling Direction
Face Cuts
1 2
3
4
Back Cuts
4
1 Inch

## Slide 35: Opposite Head Lean -- Small Diameter Tree ( Back Cut First )
Maintain Holding Wood
Holding Wood
2
3
1
Natural
Falling Direction
•
Complete the back cut first (1)
–
–
Not enough space available for both the saw blade and wedges Maintain holding wood (HW)
•
•
•
Insert two wedges into the kerf and drive them in tight Complete the face cuts (2 & 3)
Alternately drive the wedges until enough lift is achieved to fell the tree
Felling Direction
Face Cuts
2 3
1
Back Cuts
The Order Of The Cuts Is Different, But The Theory Is The Same

## Slide 36: Slight Head or Back Lean ( Slot Through Holding Wood )
Maintain Holding Wood
HW
1
2
4
Natural Falling Direction
Face the tree in the felling direction (1 & 2)
Cut slot through center holding wood to place wedge (3)
  Top of holding wood
  Bottom of holding wood (HW)
Place wedge in the kerf
  Prevents the tree from setting back on saw
  Plenty of room for saw bar and wedge
  Wedge can not hit the back of holding wood
Complete back cuts (4 & 5)
  Utilize hard plastic wedges (not steel)
  Expect to damage wedges
Finish by driving wedge and felling tree
Felling Direction
Face Cuts
1 2
4
5
5
HW
3
3

## Slide 37: Tree Sit-Back
Tree shifts in an unexpected direction
Proper cutting techniques almost always eliminate sit-backs
Use wedges at the earliest possible moment during the back cut
  If the tree sits back wedges prevent the bar from being pinched
  Holding wood prevents the tree from falling backwards
If chain saw bar becomes pinched (continue with an alternate chain saw)
Solutions to the sit-back (assume wedges were used)
Attempt to lift the tree with wedges
  Chop bark away from wedges to improve lifting efficiency
  Alternate between two or more wedges to accelerate the process
Use a driving tree (sit-back tree may fall in any direction)
Reface the sit-back tree in the direction of lean
  Second face located
    One tree diameter above the first face
    In the direction of lean
  Only fell a sit-back in the direction of lean
Get help (heavy equipment, explosives, etc.)
D
Pinched Saw Blade
HW

## Slide 38: Conclusions
Always be willing and able to walk away after assessing the tree’s lean, quality of holding wood, felling difficulty, and risk to people or property
Perform a postmortem on the stump of each felled tree to evaluate what went right and what went wrong
Choose a back cut type consistent with the length and width of the chainsaw bar
Mark up the tree in accordance with lean and falling direction like an artist marks up a canvas before painting
Through understanding of the principles associated with holding wood, stump shot, and types of back cuts allow on- the-fly cutting modifications for additional constraints

## Slide 39: References
Jepson, Jeff, To Fell A Tree—A Complete Guide to Successful Tree Felling and Woodcutting Methods, 2019.
Dent, Douglas D., Professional Timber Falling (A Procedural Approach), 1974. http://www.osha.gov/SLTC/etools/logging/mainpage.html
National Wildfire Coordinating Group, Wildland Fire Chain Saws (S-212), 2004.

## Slide 40: Estimate Tree Height Utilizing Similar Triangles
Arm
32” stick + handle
Tree Height
Ground
Add distance from face cut to human eye
Ground to
human eye
Face cut to human eye
Tree Height

## Slide 41: Estimate Crown Displacement
12” D
70' H = 840” H
1” WL
Wedge Lift (in) x Tree Height (in)
Crown Displacement (in)
Tree Diameter (in)
WL (in) x H (in)
CD (in)
D (in)
1 (in) x 840 (in)
70 (in) = 5.8 (ft)
12 (in)
Wedge
Utilizing Similar Triangles
70” CD = 5.8' CD
Tree